Water Temperature Control – Single Point of Use – Thermostatic – Rada 215

Category: Water Heater Control – Single Point of Use

Type: Thermostatic

Model: Rada 215

General:

The Thermostatic Mixing Valve (TMV) shall be of DZR brass/stainless steel/polymer construction.  TMV shall have NPT inlets and outlet with integral inlet spring loaded check valves and strainers.  TMV shall be equipped with a maximum temperature limiting and single temperature locking feature.

Materials of construction and items included shall be:

•	DZR brass/stainless steel/polymer

•	1/2” NPT inlets and outlet

•	Integral inlet check valves and strainers

•	Temperature control trim set

•	Tamperproof locking shroud

Performance: TMV shall be so designed that all of the internal operating components are enclosed in a one-piece, “sealed for life” replaceable cartridge for ease of service.  TMV shall be capable of controlling mixed water temperatures +/-2ºF at flow rates between .5 and 11.  TMV shall be capable of delivering a mixed water temperature that is within 5ºF of either inlet supply temperature.

The Thermostatic Mixing Valve shall include all of the following capabilities:

•	Maintains mixed water temperatures +/-2ºF at flow rates between .5 and 11 gpm

•	Delivers mixed water temperature within 5ºF of either inlet supply temperature

•	Operational pressure of 10 - 150 psig

•	Thermal shutdown mode upon inlet supply failure