VAFT-16 Vertical Flash Tank

Category: Vertical Flash Tank

Model: VAFT-16

Part 1	General

  - Summary

  - Submittals

  - Delivery, storage and handling

  - Warranty

Part 2	Products

  - Vertical Flash Tank

Part 3	Execution

3.01 Installation

Part 1 – General

  - Summary

- Selection Includes

  - Armstrong VAFT-16 Vertical Flash Tank

  - Submittals

- Submit the following in accordance with this specification:

  - Tag number as referred to on drawing

  - Manufacturer’s name and model number

  - Capacity and Maximum Pressure Ratings

  - Materials of construction

  - Dimensions and weights

  - All other essential data as identified in Owner’s specifications.

  - Delivery, Storage and Handling

- Receipt. Contractor or end user shall receive and store flash tanks in a manner that will protect them from weather and construction activity.

- Examination. Upon receipt, contractor or end user shall visually inspect all flash tanks for damage and compare each tank to their corresponding specification.

  - Warranty. Product shall be free from defects in material and workmanship for a period of one (1) year from date of installation, but not longer than 15 months from date of shipment from the factory.  This warranty does not extend to any product that has been subject to misuse, neglect, or alteration VAFTer shipment from Armstrong factory.

Part 2 – Products

  - Vertical Flash Tank

- Acceptable Manufacturers

  - Armstrong Intl, Inc. VAFT-16 Vertical Flash Tank

- The VAFT-16 flash tank shall be a carbon steel ASME code Sec. VIII “U” stamped vessel rated for 150 psig maximum vessel pressure.

- ASME code carbon steel flash tank shall measure 16” x 48” and have a maximum overall height of 63-1/2”.

- Flash tank shall have one (1) 6” 150# flanged tangential inlet, one (1) 6” 150# flanged vent, one (1) 2” NPT bottom drain, one ½” NPT pressure gauge connection and one (1) 2” NPT safety relief valve connection.

- The vertical flash tank must be capable of handling up to 20,000 lb/hr condensate and up to 3000 lb/hr flash steam.

- Connections sizes and locations shall be as shown on drawing CDF1023.

- Manufacturer’s standard painting will apply.

Part 3 – Execution:

  - Installation

- Installation Compliance. Install in accordance with manufacturer’s instructions and as shown on the drawing.

- Insulation. Install the removable insulation cover in accordance with manufacturer’s instructions.

End of Section